## Slide 1
MYODRUM
A muscle-controlled virtual instrument using EMG and IMU sensing
[Author full name 1] | [Author full name 2] | Project 26P02
Why MyoDrum?
Can muscle activity and arm motion identify intentional air-drumming strikes and choose a virtual drum quickly enough for interactive play?
Goal: an affordable wearable instrument that turns natural drumming gestures into sound.
WORKING TWO-STICK PROTOTYPE
Two MPU6050 sensors + four active EMG channels
FOUR EMG CHANNELS
A0
Left forearm
A2
Left triceps
A3
Right forearm
A4
Right triceps
Six-channel expansion follows the four-channel comparison.
How MyoDrum works
EMG
muscle activity
IMU
stick movement
SYNCHRONIZED
SENSOR WINDOW
CHOOSE A
CLASSIFIER
PLAY
SOUND
The IMU describes what the stick did. EMG helps decide whether the movement was intentional.
KICK • SNARE • CRASH
Rule-based classifier - working now
1
IMU proposes
A fast movement, reversal and acceleration change create a strike candidate.
2
EMG confirms
The active arm must cross its own calibrated muscle threshold.
3
Safeguard
Cooldown and return travel suppress double or triple sounds.
Bagged-tree classifier - next stage
One labelled
sensor window
Motion + muscle
features
Many decision
trees
Each tree votes: NO HIT | KICK | SNARE | CRASH
MAJORITY VOTE = FINAL PREDICTION
A group of trees should be less sensitive to one noisy electrode or one unusual swing than a single tree.
Virtual drum zones
SNARE
left pose
KICK
centre / down
CRASH
raised / right
Zones are defined relative to a calibrated neutral pose, not by double-integrated position.
Built hardware
6 EMG BOARDS
Signal conditioning, power and Arduino Mega 2560
Machine-learning data status
3
sessions
72
labelled blocks
1,080
requested hits
NEXT: TRAIN → TEST ON AN UNSEEN SESSION
WHAT STILL NEEDS TESTING
• held-out accuracy
• false-trigger rate
• sound latency
• orientation drift
• 6-channel benefit
Accepted versus rejected strike: synchronized IMU and EMG
Chart: Time relative to accepted decision (s)
ACCEPTED: IMU + EMG align
REJECTED: EMG stays below threshold
Real right-hand events from session_20261012_165912. The accepted decision occurs at 0.00 s; the EMG-timeout rejection follows 0.51 s later.
Performance metrics by operating mode
Chart: Validated evidence (%)
| IMU only | EMG only | IMU + EMG rule-based | IMU + EMG ML | Rule + ML hybrid
Correct-drum accuracy | 0 | 0 | 0 | 0 | 0
End-to-end latency | 50 | 50 | 50 | 0 | 0
Median decision delay | 0 | 0 | 100 | 0 | 0
Noise rejection | 0 | 0 | 50 | 0 | 0
Simultaneous-hit success | 50 | 0 | 50 | 0 | 0
0% = not measured 50% = partial evidence 100% = measured result
Current result: rule-based median decision delay = 0 ms (95th percentile = 125 ms).
Accuracy = correct drum selections ÷ intended strikes × 100%. A 0% evidence bar means unmeasured, not zero system accuracy.
CONCLUSION
MyoDrum already combines synchronized motion and muscle sensing for three virtual drums. The next step is to train the bagged-tree model and compare it fairly with IMU-only, EMG-only and rule-based fusion.
References: TDK InvenSense, MPU-6050 Product Specification; SENIAM, Sensor Locations; MyoDrum recorded sessions. *Classifier delay excludes speaker/Bluetooth audio latency.
Notes: Poster evidence sources:
Project repository: C:\Users\ndlov\OneDrive\Desktop\FinalMyodrum
Synchronized strike plot: data/raw/session_20261012_165912/imuEmgStream.mat.
Rule-based thresholds: common/myoDrumConfig.m and classifiers/ruleBased/*.m.
ML collection summary: sessions 20261013_182950, 20261014_103705 and 20261014_110441.
Institutional layout reference: C:\Users\ndlov\Downloads\In_Person_Poster_Guidelines.pptx
Background artwork generated for this poster with OpenAI image generation; drum illustration supplied by the user.
External references shown on poster: TDK InvenSense MPU-6050 product specification; SENIAM sensor location guidance.